## Slide 1: Seamless MPLS
Vinit Jain
Cisco Systems Inc.
Twitter - @vinugenie

## Slide 2: Agenda
Mobile Transport Market Conditions
Seamless MPLS Overview
Seamless MPLS Components
Seamless MPLS Architecture Models
Summary

## Slide 3: Mobile Transport Market Conditions
High Capacity requirements from Edge to Core
  100Mbps eNB, 1Gbps Access, 10Gbps Aggregation, 100Gbps Core
Higher scale as LTE drives ubiquitous mobile broadband
  Tens- to hundred-of-thousands of LTE eNBs and associated CSGs
Support for multiple and mixed topologies
  Fiber and microwave rings in access, fiber rings, hub and spoke in aggregation and core networks
Need for graceful service integration and integration into existing infrastructure
Need to support transport for all services from all locations
Optimized operations with consistent packet transport

## Slide 4
Core
Edge
Aggregation
Access
IP/MPLS
Cross-Domain Convergence
MPLS as Network Convergence Technology Optimizing Service Delivery
LS Challenges with differing Access technologies
  Complexity of achieving 50 millisecond convergence with TE-FRR
  Splitting large networks into domains while delivering services end-to-end
  Common end-to-end convergence and resiliency mechanisms
  End-to-end provisioning and troubleshooting across multiple domain
Unified MPLS addresses these challenges
with elegant simplicity and scale

## Slide 5: Seamless MPLS Overview
An efficient MPLS transport architecture
Virtualized to support many services on one infrastructure
Relying on an intelligent hierarchy to scale to new challenges
Enabling seamless operation for network and service resilience
Separating transport from service operations with single touch point service enablement and contiguous OAM
Integrating alternate access technologies on same infrastructure while still enabling Fixed and Mobile Services

## Slide 6: Seamless MPLS Operation Transport & Service Decoupling
MPLS
MPLS
MPLS
Typically, a service has to be configured on every network element via operational points. The management system has to know the topology.
Goal is to minimize the number of operational points
Only with the integration of all MPLS islands, the minimum number of operational points is possible
Service provisioning only at the Edge
Unified MPLS
Access
AGG
AGG
LER
LSR
LER
AGG
AGG
Access
Operational Points

## Slide 7: Unified MPLS = Classical MPLS with a few additions
RFC 3107
BGP filtering
LFA R-LFA
BGP PIC
IGP/LDP Domain isolation
E2E OAM
Classical MPLS
Scalability
Security
Simplification
Multi-Service
Unified
MPLS
Architecture
Flex Access L2/IGP/BGP/MPLS-TP/LDP DoD

## Slide 8: RFC-3107
RFC 3107 was approved May 2001, main purpose being scaling of MPLS
RFC 3107 is BGP IPv4 with the ability to distribute labels
BGP Filtering supported via BGP Communities in a secure manner
RFC 3107 basis:
BGP can be used to distribute MPLS labels in the same way it can distribute a route
The label mapping information for a particular route is piggybacked in the same BGP Update message that is used to distribute the route itself.
  If two immediately adjacent Label Switched Routers (LSRs) are also BGP peers, then label distribution can be done without the need for any other label distribution protocol.

## Slide 9: LFA & R-LFA
What is LFA FRR?
  RFC 5286 basic fast re-route mechanism with local protection in pure IP and MPLS/LDP networks
  Pre-computing available paths at source node that do not create loops
  Gives benefits of TE-FRR, but no configuration or design required
What is Remote LFA?
  Defined in draft “http://tools.ietf.org/html/draft-shand-remote-lfa”
  Remote LFA uses automated IGP/LDP behavior to extend basic LFA FRR to arbitrary topologies
  A node dynamically computes its remote loop free alternate node(s)
    Done during SFP calculations using PQ algorithm (see draft)
  Automatically establishes a directed LDP session to it
    The directed LDP session is used to exchange labels for the FEC in question
  On failure, the node uses label stacking to tunnel traffic to the Remote LFA node, which in turn forwards it to the destination

## Slide 10: Remote LFA FRR - Protection
C2’s LIB
  C1’s label for FEC A1 = 20
  C3’s label for FEC C5 = 99
  C5’s label for FEC A1 = 21
On failure, C2 sends A1-destined traffic onto an LSP destined to C5
  Swap per-prefix label 20 with 21 that is expected by C5 for that prefix, and push label 99
When C5 receives the traffic, the top label 21 is the one that it expects for that prefix and hence it forwards it onto the destination using the shortest-path avoiding the link C1-C2.
A1
C1
C2
C3
E1
C4
A2
Backbone
Access Region
C5
Directed LDP
session
21
20
99
21
99
21
X
21

## Slide 11: BGP Prefix-Independent Protection (PIC)/BGP FRR
BGP Fast Reroute (BGP FRR) enables BGP to use alternate paths
Algorithm uses a pointer to move all prefixes to new next hop, not a hop by hop rewrite
~ 100 msec protection
Prefix-Independent
Default behavior, entirely automated computation
Enables 3107 BGP+labels operation to scale via hierarchy while maintaining fast convergence characteristics
For Transport and Service convergence

## Slide 12: Unified MPLS Architecture Models
Architecture Models based on:
  Access Type: Ethernet TDM or MPLS access
  Network Size: Small/Medium (1000 nodes or less) or Large
  End to Labeled Switch Path
Deployment Model | Network Size | Access Type | Core/Aggregation LSP
1 | Small/Medium | Ethernet/TDM | Flat LDP
2 | Small/Medium | MPLS | Hierarchical Labeled BGP
3 | Large | Ethernet | Hierarchical Labeled BGP
4 | Large | MPLS | Hierarchical Labeled BGP for Core, Aggregation and Access
5 | Large | MPLS | Hierarchical Labeled BGP for Core, Aggregation with redistribution in Access
Notes: - Clarify = How large is large (# of routers?) ?

## Slide 13: 1 – Small Network: Ethernet/TDM Access
Core and Aggregation Networks form one IGP and LDP domain.
  Scale recommendation is less than 1000 IGP/LDP nodes
Packet Microwave links aggregated in Aggregation Nodes
Mobile Access is based on TDM
All services –Mobile and Wireline– enabled by Aggregation Nodes
Flat LDP LSP across Core and Aggregation Networks
Distribution Node
Core and Aggregation
IP/MPLS Domain
Core Node
Aggregation
Node
Core Node
Core Node
Core Node
IGP/LDP domain
Aggregation Node
Aggregation Node
Aggregation Node
Aggregation Node
Pre-Aggregation
Node
IP/Ethernet
Fiber and Microwave
3G/LTE
TDM and Packet Microwave, 2G/3G/LTE
Mobile
Transport GW
Mobile
Transport GW
Business
CSG
Notes: Core and Aggregation Networks form one IGP and LDP domain.
    With small aggregation platforms the scale recommendation is less than 1000 IGP/LDP nodes.
  All Mobile (and Wireline) services are enabled by the Aggregation Nodes. The Mobile Access is based on TDM and Packet Microwave links aggregated in Aggregation Nodes enabling TDM/ATM/Ethernet VPWS and MPLS VPN transport

## Slide 14: 2 – Small Network: MPLS Access
The Core and Aggregation form a relatively small IGP/LDP domain (1000 nodes)
MPLS enabled RAN, each RAN forms a different IGP/LDP domain
The Core/Aggregation and RAN Access Networks are integrated with labelled BGP LSP
The Access Network Nodes learn only the MPC labelled BGP prefixes and selectively and optionally the neighbouring RAN networks labelled BGP prefixes.
Hierarchical BGP LSP Across Core + Aggregation and Access Networks
Core and Aggregation
IP/MPLS domain
IGP Area
Aggregation Node
Aggregation Node
Aggregation Node
Aggregation Node
Pre-Aggregation
Node
RAN
IP/MPLS Domain
LDP LSP
LDP LSP
LDP LSP
iBGP Hierarchical LSP
RAN
IP/MPLS Domain
Pre-Aggregation
Node
Mobile
Transport GW
Core Node
Core Node
Core Node
Core Node
Mobile
Transport GW
CSG
CSG
CSG
CSG
CSG
CSG
Notes: The Core and Aggregation form a relatively small IGP/LDP domain (1000 nodes)
The RAN is MPLS enabled. Each RAN network forms a different IGP/LDP domain
The Core/Aggregation and RAN Access Networks are integrated with labelled BGP LSP
The Access Network Nodes learn only the MPC labelled BGP prefixes and selectively and optionally the neighbouring RAN networks labelled BGP prefixes.

## Slide 15: 3 – Large Network: Ethernet/TDM access
Core Network
IP/MPLS Domain
IP/Ethernet
Fiber and Microwave
3G/LTE
Core and Aggregation Networks enable Unified MPLS Transport
Core and Aggregation Networks are organized as independent IGP/LDP domains
Core and Aggregation Networks may be in same or different Autonomous Systems
The network domains are interconnected with hierarchical LSPs based on RFC 3107, BGP IPv4+labels
No MPLS in Access Domain
Aggregation Node enable Mobile and Wireline Services over Unified MPLS transport.
Hierarchical BGP LSP Across Core Network and Aggregation Networks
Pre-Aggregation Node
Aggregation Network
IP/MPLS
Domain
Aggregation Node
Aggregation
Node
Aggregation Network
IP/MPLS
Domain
Core
Node
LDP LSP
LDP LSP
LDP LSP
iBGP (eBGP across ASes) Hierarchical LSP
TDM and Packet Microwave, 2G/3G/LTE
Aggregation Node
Aggregation Node
Aggregation Node
Core
Node
Core
Node
Core
Node
Mobile
Transport GW
Mobile
Transport GW
CSG
CSG
Notes: The Mobile Core and Aggregation Networks enable Unified MPLS Transport
The Core and Aggregation Networks are organized as independent IGP/LDP domains
Core and Aggregation Networks may be in different Autonomous Systems, in which case the inter-domain LSP is enabled by labeled eBGP in between ASes
The network domains are interconnected with hierarchical LSPs based on RFC 3107, BGP IPv4+labels. Intra domain connectivity is based on LDP LSPs
The Aggregation Node enable Mobile and Wireline Services. The Mobile RAN Access is based on TDM and Packet Microwave.

## Slide 16: 4 – Large Network: MPLS Access
Core, Aggregation, Access Network enable Unified MPLS Transport
Core, Aggregation, Access are organized as independent IGP/LDP domains
Core and Aggregation Networks may be in same or different Autonomous Systems
Network domains are interconnected with hierarchical LSPs based on RFC 3107, BGP IPv4+labels.
Intra domain connectivity is based on LDP LSPs
The Access Network Nodes learn only the required labelled BGP FECs
Hierarchical BGP LSP Across Core, Aggregation and Access Networks
RAN
IP/MPLS
domain
Core Node
Core Node
Core Node
Core Node
LDP LSP
LDP LSP
LDP LSP
LDP LSP
LDP LSP
iBGP (eBGP across ASes) Hierarchical LSP
RAN
IP/MPLS
domain
Core Network
IP/MPLS Domain
Pre-Aggregation Node
Aggregation Network
IP/MPLS
Domain
Aggregation Node
Pre-Aggregation
Node
Aggregation Network
IP/MPLS
Domain
Core
Node
Aggregation Node
Aggregation Node
Aggregation Node
Core
Node
Core
Node
Core
Node
Mobile
Transport GW
Mobile
Transport GW
CSG
CSG
CSG
CSG
CSG
CSG
Notes: The Mobile Core, Aggregation, Access Network enable Unified MPLS Transport
The Core, Aggregation, Access are organized as independent IGP/LDP domains
Core and Aggregation Networks may be in different Autonomous Systems, in which case the inter-domain LSP is enabled by labeled eBGP in between ASes
The network domains are interconnected with hierarchical LSPs based on RFC 3107, BGP IPv4+labels. Intra domain connectivity is based on LDP LSPs
The Access Network Nodes learn only the required labelled BGP FECs, with selective distribution of the MPC and RAN neighbouring labelled BGP communities

## Slide 17: 5 - Large Network, MPLS Access
Core and Aggregation are distinct IGP/LDP domains that enable inter domain hierarchical LSPs
Core and Aggregation Networks may be in same of different Autonomous Systems
Redistribution of Core/Aggregation LSPs into Access Networks IGP
Hierarchical BGP LSP with IGP/LDP Redistribution in Access Network
RAN
MPLS/IP
IGP Area/Process
RAN
MPLS/IP
IGP Area/Process
MPC iBGP community
into RAN IGP
RAN IGP CSN Loopbacks
into iBGP
Core
Core
Core
Core
LDP LSP
LDP LSP
LDP LSP
LDP LSP
LDP LSP
i/eBGP Hierarchical LSP
Core Node
Core Node
Core Node
Core Node
Core Network
IP/MPLS Domain
Aggregation Network
IP/MPLS
Domain
Aggregation Node
Pre-Aggregation
Node
Aggregation Network
IP/MPLS
Domain
Core
Node
Aggregation Node
Aggregation Node
Aggregation Node
Core
Node
Core
Node
Core
Node
Mobile
Transport GW
Mobile
Transport GW
Pre-Aggregation
Node
MPC iBGP community
into RAN IGP
RAN IGP CSN Loopbacks
into iBGP
CSG
CSG
CSG
CSG
CSG
CSG
Notes: The Core and Aggregation are organized as distinct IGP/LDP domains that enable inter domain hierarchical LSPs based on RFC 3107, BGP IPv4+labels and intra domain LSPs based on LDP
Core and Aggregation Networks may be in different Autonomous Systems, in which case the inter-domain LSP is enabled by labeled eBGP in between ASes
The inter domain Core/Aggregation LSPs are extended in the Access Networks by distributing the RAN IGP in the AggregationIPV4 unicast + label iBGP and the Mobile Transport Gateways labeled iBGP prefixes into RAN IGP.

## Slide 18
Sample End-to-End Unified MPLS Architecture
Routing Isolation and Label Stack for LSP between Pre-Agg. Node Loopbacks
  No IGP route is propagated from Aggregation to the Core. IGP area has routes for that area only plus routes to core ABRs. Only the core ABR’s are propagated from L2 to L1
  LDP labels are used to traverse each domain and reach core ABRs
  BGP labels are used by Labeled BGP PEs & ABRs to reach Labeled BGP PEs in remote areas
  Service (e.g. PW) labels are used by Label BGP PEs
Core Network
Core ABR
(Inline RR)
Pre-Agg.
Node
Access
Network
Agg. Node
MPC
Gateway
Access
Node
Centralised RR
Agg. Node
Core ABR
(Inline RR)
Access
Node
Pre-Agg.
Node
Core ABR
(Inline RR)
Core ABR
(Inline RR)
Access
Network
Agg. Node
Agg. Node
Aggregation
Network
Aggregation
Network
ISIS Level 1/OSPF x
ISIS Level 1/OSPF x
ISIS Level 2/OSPF 0
L2
L2
IGP/LDP Label
BGP3107 Label
Service Label
Push
Push
Swap
Pop
Push
Swap
Pop
Swap
Swap
Swap
Pop
LDP LSP
LDP LSP
LDP LSP
BGP LSP

## Slide 19
Cell Site
Access
Layer
Aggregation
Layer
PGW
SGW
Aggregation
node
Distribution
node
Ethernet uW
Fibre
Cell site
Router
Pre-Aggregation
Layer
Core
node
Core Network
Aggregation Network
Unified MPLS Architecture
Summary
Aggregation Node
Core ABR
Sample Routing Architecture
IGP/LDP
IGP/LDP
L2
Ring
iBGP/eBGP
Core
Layer
Core ABR
Pre-Aggregation
Node
Access
Network
IGP/LDP
Aggregation Node
EPC Gateway
Access Node
Access Node
Centralised RR
Flexible L2 & L3 transport virtualisation to support GSM, 3G & LTE, wholesale & retail options
New levels of Scale for MPLS transport and optimal routing through RFC 3107 with BGP hierarchical LSPs
Simplified MPLS Transport with E2E OAM, performance management, provisioning with seamless resiliency
Notes: Core, Aggregation, and Access partitioned as independent IGP/LDP domains.
  Reduce size of routing & forwarding tables on routers to enable better stability & faster convergence.
LDP used to build intra-domain LSPs within domains
RFC 3107 BGP IPv4+labels used as inter-domain label distribution protocol to build hierarchical LSPs across domains
Inter-domain LSPs are extended to RAN Access with controlled redistribution based on IGP tags and BGP communities.
  Preserve low scale in RAN IGP: Only local RAN IGP prefixes + few Mobile Packet Core loopbacks
Intra-domain link & node failures protected by LFA FRR*, and ABR failures protected by BGP PIC*

## Slide 20: Thank You